# Chem&Soc – Chemistry & Environment

## Air Pollution

Pollution is the introduction of waste matter or energy into the environment so that caused damage or deterioration to living systems or environment

### Air Pollution:

Major pollutant: CO, SO2, nitrogen oxides, hydrocarbons, O3, Particulates

Formed during combustion of fossil fuels

Pollutants & their effect:

| Pollutants | Source | Effect |
| --- | --- | --- |
| Carbon monoxide | Incomplete burning of carbon-containing fuels | 1. Failure of hemoglobin to carry oxygen in blood 2. Causes death |
| Sulphur dioxide | Burning fossil fuels | 1. Damage to respiratory systems 2. Increase in asthma attacks 3. Formation of acid rain |
| Nitrogen oxides | 1. Petrol or diesel-burning engines 2. Coal or oil furnaces | 1. Formation of photochemical smog 2. Damage to lung tissues and blood vessels 3. Formation of acid rain |
| Hydrocarbons | 1. Evaporation of organic materials 2. Car exhaust | 1. Formation of photochemical smog 2. Carcinogenic |
| Ozone | Reaction of oxygen with free oxygen atom | 1. Eye irritation 2. Aggravates asthma 3. Damage to plants 4. Early deterioration of rubber and fabrics |
| Particulates | 1. Refuse incineration 2. Factories 3. Diesel vehicles 4. Construction sites 5. Coal/charcoal burners | 1. Constriction of respiratory passage 2. Damage to lung tissues 3. Respiratory illness 4. Carcinogenic |

Concentration of pollutants are described by part per million, ppm

ppm:	No. of pollutant molecules per one million air molecules
 		= No. of unit volume of pollutant per a million unit volume of air

Alternative unit: Microgram per cubic meter gm–3

Mass of pollutant in 1m3 volume of air

ppm and gm–3 can be interconverted by ideal gas law: PV = nRT

Acid rain: Rain water w/pH value  5.6

Formation due to acidic gaseous product (SO2, NO2)

Acid rain can damage plants, aquatic organisms, metal / stoneworks, deteriorates building, rocks and statue

Photochemical smog: Smog formed under the influence of sunlight

Smog = Smoke + Fog

Photochemical smog is a mixture of pollutants including particulates, nitrogen oxides, O3, aldehydes, peroxyactyl nitrate (PAN), hydrocarbons, etc.

Irritating brownish haze

Causes headaches, Irritation to eye, nose & throat, Impairing lung functions, Cough & wheeze

### Ozone:

Ozone (O3) is a pale blue gas with pungent chlorine-like odor

O3 is formed at stratosphere (20-50 km above the ground) by absorption of UV:

Absorbs UV of =250nm

O3 in stratosphere is then absorbs UV of =215-295nm to dissociation

Photodissociation:

Ozone-oxygen cycle screens 99% UV radiation

Thinning of ozone layer: Skin cancer, Eye cataract, Decrease in yield of crops

### Chlorofluorocarbons:

CFCs: A family of compound containing Cl, F, C

Usage:

Aerosal propellants

Liquid state in pressurized cansVapor

Solvents in cleaning electronic components & metals

Refrigerants: Since CFC is non-toxic & non-corrosive

Safer

Absorb heat of vaporization to cool surroundings

Blowing agents in manufacture of foam plastic

CFCs has long lifetime, light, unreactive & non-biodegradable

Accumulates in high levels of atmosphere (stratosphere)

Under UV, CFC dissociates and gives Cl free radicals

A series of chain reactions to destroy ozone

Depletion of ozone

Alternatives for CFCs:

Hydrochlorofluorocarbons: Less stable, break down quickly in atmosphere

Could still damage ozone layer if overused though it has a lower ozone depletion potential

Hydrofluorocarbons: Has no chlorine and ozone safe, but it is toxic

Hydrocarbons: Contain no Cl and ozone safe, but flammable and poisonous

## Water Pollution

### Water Pollution:

Water pollution is the degeneration of the quality of water by the introduction of chemical, physical & biological wastes into rivers, streams, lakes & oceans

Pollutants & effects:

| Pollutant | Harmful Effect |
| --- | --- |
| Livestock waste | Release noxious gases Lead in the death of aquatic organisms |
| Oil spillage | Clog the feathers of sea birds and prevent them from flying or swimming Interfere with the insulation of the feathers of birds Poison birds by ingestion Prevent dissolution of oxygen Spoil recreational resorts |
| Residues of pesticides | Toxic Accumulate along food chains Potential for damaging internal organs Harmful on reproduction of animals |
| Detergents in sewage | Cause eutrophication Foaming in rivers and lakes Lead to the death of aquatic organisms |
| Industrial effluents | Toxic Accumulate along food chains |

### Water Quality:

Dissolved oxygen (DO) is used as an indicator of oxygen content in water

Measured in mg dm–3 or percentage saturation

Fish need 4-5 mg dm–3 DO to survive

Depletion of oxygen maybe caused by biological degradation of waste matter

Biological oxygen demand (BOD) is the amount of oxygen required to break down organic matter present in water

High BOD = Lots of organic matter in water

Low BOD = Little organic matter in water

Natural water has BOD of 1-4 mg dm–3

If BOD  Oxygen replenished, Aquatic organism may die and organic debris will accumulate

Producing unpleasant odor & taste

Five day BOD (BOD5) is a measure for oxygen consumed in a water sample at 20°C for 5 days

BOD5 = (DO at first day) – (DO after fifth day)

## Solid Waste

### Solid Waste:

Solid waste is produced by domestic households, commercial & manufacturing industries, construction sites

Domestic waste contain 40% of Paper, plastic and metals

Disposal of solid waste:

Incineration:	Reduces wastes of 85% volume
 	Kills disease-causing organisms
 	No water pollutant, but polluting atmosphere with toxic gas

Landfilling: Wastes are compressed and covered with earth on landfill sites

May produce landfill gas (methane) and leachate (highly polluting water)

### Pollution problems associated with the disposal of plastics:

Plastics are tailored for long life

Do not decompose after long time

Delaying the reuse of landfill sites

Incineration of plastic causes air pollution

Evolves HCl, etc.

Dispose plastic in sea endangers aquatic life as plastic fragments clogged their digestive tracts or suffocates them

Solution: Develop degradable plastics or Recycling

Biopolymers: Polymers that can be made by micro-organisms

Photodegradable: Contains C=O group

Biodegradable: Contains starch / cellulose

## Pollution Control in Hong Kong

### Air pollution:

Use of unleaded petrol

Lead cpd was added to petrol to prevent knocking but it’s toxic

Install catalytic converter

Made of rhodium and platinum / palladium

2 NO(g) + 2 CO(g)  N2(g) + 2 CO2(g)
2 CO(g) + O2(g)  2 CO2(g)
CnHm + O2(g)  CO2(g) + H2O(g)

Catalytic converter work only on unleaded petrol

Limited the sulphur content in fuels

Reduce sulphur dioxide emissions from burning fossil fuels

Desulphurization of flue gas

Further decrease SO2 emissions in coal-fired plant

The flue gas desulphurization system (FGD) uses wet limestome-gypsum scrubbing process to remove 90% SO2 from flue gas

SO2(g) + H2O(() (( H2SO3(aq)

CaCO3(s) + H2SO3(aq) (( CaSO3(s) + CO2(g) + H2O(()

CaSO3(s) + ½O2(aq) (( CaSO4(s)

CaSO3(s) + ½H2O(() (( CaSO3··½H2O(aq)

CaSO4(s) + 2H2O(() (( CaSO4··2H2O(aq)

Electrostatic precipitation in Power Plants:

Removes 99% the fly ash precipitated in flue gas beforereleasing itno atmosphere

Use of low nitrogen oxide burners

By using modified conditions (lowered temperature) to reduce the nitrogen oxides formation by 50%

### Sewage Treatment:

Primary treatment

Removes 60% solid, Reduces BOD by 35%

Screens the large objects and grit particles

To primary sedimentation tanks to settle out suspended solids

Removed as sludge

Secondary treatment

The effluent is then moved to aeration tanks to mix with air and micro-organisms

Digests organic matter

Removed overall 90% solid as sludge and reduced 95% BOD

The effluent is then chlorinated to kill micro-organisms and then discharged or further treated to remove NO3– or PO3–

Tertiary treatment

Sludge treatment

The sludge removed is then treated to remove pathogen / reduce volume / biodegrade organic matter

Produces biogas (methane)

The treated sludge is dried and disposed to landfill sites

### Treatment of Chemical Wastes:

Chemical waste is produced by electroplating, electronic, electrical industries and scientific product manufacturer

Chemical waste: Acid, Alkali, Organic solvents, Cyanide, Heavy metals, Oily waste

They are corrosive, flammable, poisonous and give off toxic explosive vapor

Treatment of chemical waste in chemical waste treatment center:

- Oil-water separation system

Recovers waste oil from oily water mixture

- Physical-Chemical treatment system

Separates oil from oily water and water from residues

Neutralize acids and bases

Use slaked lime to neutralize acid: Ca(OH)2 + 2H3O+ (( Ca2+ + 4H2O

Use sulphuric(VI) acid to neutralize alkali

Removes metals from metal-containing waste by alkali
  Mn+ + nOH– (( M(OH)n(s)

Precipitation

Reduction of Cr(VI) cpd to Cr(III) cpd

Cr(VI) is a soluble toxic cpd in effluent of metal-finishing plants

It is reduced to non-toxic Cr(III) then precipitated
  2H2CrO4(aq) + 3Na2SO3(aq) + 3H2SO4(aq) (( Cr2(SO4)3(aq) + 3Na2SO4(aq) + 5H2O(()
  Cr2(SO4)3(aq) + 6NaOH(aq) (( 2Cr(OH)3(s) + 3Na2SO4(aq)

- High temperature Incineration

Decomposing toxic organic cpds & cyanides to CO2, H2O and various gases

It reduces the bulk of the waste and eliminating the problem of liquid waste disposal