# Physics - Electricity & Magnetism

## Electrostatics

Electric field is a region where an electric force can be experienced by a test charge

Electric field intensity is the electric force experienced by a unit of positive charge

Unit: NC–1, Vm–1

### Coulomb’s Law:

The force between charged particles is proportional to the product of the charges and inversely proportional to the square of the distance between them

Electric force

 = Permittivity of the medium

Unit: C2N–1m–2 or Fm–1

 = Permittivity of free space = 8.85(10–12 C 2 N–1 m–2

Permittivity of air in STP = 1.0005

Relative permittivity

In vacuum,  = 8.988(109 m F–1 ( 9.0(109 Nm2C–2

Electric force

Electric field intensity

Shell theorem states that a uniform spherical shell of charge behaves, for external points, as if all the charges were concentrated of its center.  For charged particles placed inside, no force is exerted by the shell.

### Field Lines:

Field lines are lines of force in electric field

Represent an electric field pictorially

Direction of tangent of the field line represents the direction of force acting on a positive test charge

Density of field line is proportional to the magnitude of electric field

Field lines form no closed loops, nor intersects

Lines start at the positive charge and end at negative charges

Number of lines attached to a charge is proportional to the magnitude of charge

Electric Potential Energy of a charge q at point P is the work done by a force bringing the charge from infinity to point P

Electric

At infinity, the electric P.E. of any charge is defined to be 0

A system tends to have minimum U, thus:

Like charges have U  0 and repulsion decreases the U towards 0 at infinity separation

Unlike charges have U  0 and attraction decreases the U towards –( at zero separation

Electric potential V at point P is the electric potential energy U per unit charge

Unit: JC–1, Volt V

Electron-volt is a unit of energy, 1 eV = 1.602(10–19 J

Electric force F =

Negative sign indicates that electric force points to lower U

Electric field intensity E =

### Uniform plate

E-field btw two plates are uniform

P.d. btw two plates is given by

V = Ed	( 	E-field btw the plates:

### Equipotential

Equipotentials are lines / surfaces / volumes joining the pts of the same electric V together

Field lines ( Equipotentials

Equipotentials of field by a point charge are sperical surface

Equipotentials btw a pair of charged plates are ( to the plates and parallel

Surface charge density is the charge per unit surface area, i.e.

 is higher on the curved surface than on the flat surface

 is higher on the curve of smaller radius of curvature

### Conductors

Inside a conductor, E = 0

Surface of a conductor is an equipotential

V inside a conductor = V on conductor surface = Constant

Charge distribution on a conductor can easily affected by another conductor

Electric induction

The E-field established by a charge inside the cavity of a hollow conductor is unaffected by the

E-field outside

Electrostatic shielding

Spherical conductors can be used to store charge

Conductors of small radius of curvature can produce very large E-field by a low V

If the E-field is too strong in air, e– of air molecules would be pulled away and forms ion-pairs

Corona discharge

E-field that causes corona discharge is called the breakdown field strength, Eb

## Current Electricity

Current is the rate of flow of charge at a particular cross section, i.e.

### Drift velocity:

Free electrons inside a conductor moves randomly as a result of possessing thermal energy

Electrons moves in a zig-zag path

Resultantly, no net displacement and no net KE lost/gain

No net current

When electric p.d. applied, electrons are accelerated against the E-field, then still in random motion

e– gain velocity & KE

Electrons attain a steady average drift velocity towards the high V region

### Charge & Current

n electrons per unit volume

Drift velocity = v

Cross-sectional area of charge flow = A

Total charge pass thou’ a plane P in time t:  Q = nAvet		where e = Charge of an e–

Current:

Current density:

### Voltage & Power

Electromotive force: Energy transferred to a unit charge passing thou’ a source

Unit: V, JC–1

Potential difference btw two pts in a circuit is the amt of electrical energy changed to other form of energy when a unit charge passed from one pt to another pt along the circuit

Unit: V, JC–1

Power generated by a source: P = I

Power disspated btw to pts of the circuit: P = IV

### Resistance

Resistance express the reluctance of circuit element to allow charge to press thou’

Ohm’s Law: V ( I

V = R I

Energy is given up to the ions when e– collides with metal ions in metallic lattice

e– loss KE, ions gain KE

Power of heating effect:

A conductor’s resistance R is directly proportional to its length  and inversely proportional to its cross-sectional area A

 = Resistivity, unit: m

Resistance of a material changes as temperature

- R = R0 (1+)		: 	Temperature in oC
								R0: 	Resistance in 0 oC

 = Temperature coefficient, unit: oC–1

  0 	(

  0 	(

### Voltage & Current

Circuits in series, the current is a constant

- In series,

Circuits in parallel, the voltage is constant

- In parallel,

Kirchhoff’s First Law: Algebric sum of current at a junction of a circuit is 0.

Kirchhoff’s Second Law: The potential difference in a closed loop is 0.

### Efficiency

In a circuit with a load R and a power source  with internal resistance r, the maximum current is:
			when R = 0

P.d. across R :

Power delivered to R :

Efficiency:

Maximum PR is  when R = r

Maximum PR	 (	 = 50%

## Measuring Devices

### Wheatstone Bridge:

Null deflection in galvonometer 	( 	VAB = 0

The resistance of one resistor can be calculated when other 3 are known

### Meter Bridge:

Consists of a resistance wire and a jockey

The resistance wire usually use a uniform resistance for convenience reason

When the bridge is balanced:

Galvanometer’s reading = 0

### Internal resistance:

for some constant k

### Voltmeter & Ammeter:

In a circuit with a load of high resistance:

Circuit:

VR + VA ( VR  as VA is negligible.

Nominal resistance

Nominal R  Actual R

If the load is of low resistance, VA is comparable with VR

In a circuit with a load of low resistance:

Circuit:

IV + IR ( IR  as IV is negligible.

Nominal resistance

Nominal R  Actual R

If the load is of high resistance, IV is comparable with IR

## Capacitors

Capacitor is a device of two conductors separated by a dielectric for storing charges

### Charging & Discharging:

When a capacitor is connected to a battery,

Negative charges are pushed out of negative terminal

Positive terminal draws in negative charges

Negative plate of cap bears charges –Q
Positive plate of cap bears charges +Q

Total charges of the capacitor = 0

Flow of charges from battery to capacitor continues until p.d. btw two plates = E.M.F. of battery

Current of charging:

Q on the plate ( V across plates

Q = C V		for some proportionality constant C

C = Capacitance

Unit: Farad (F), CV–1

When the terminals of the capacitor are shorted,

Electrons flows from negative plate to positive plate via external circuit

Opposite charges are neutralized

Eventually, p.d. btw plates: V = 0

Current of discharging:

### Leaking

When cap. is connected to ext. element while charging, some charge will leak thou’ that element

When charging voltage exceed the max. voltage, leaking also occur

Leaking capacitor = A cap. w/a resistor connected parallel with it

### Reed switch

N, F are fixed;  K is movable

F, K are made of ferromagnetic material;  N is non-ferromagnetic

N is closed normally;  K is opened normally

If there is no current thou’ the coil, N, K are in contact

If a large-enough current passing thou’ the coil, F, K are in contact

### Measuring capacitance

E.M.F. of the DC power source = V
Discharging current = I
Frequency of the AC source = f
Resistance of the rheostat = R
Capacitance of capacitor = C

Adjusting suitable R, C can be charged and discharged completely in one cycle

Average discharging current: I = f Q = f C V

Capacitance

### Parallel plate capacitor:

Parallel plate capacitor consists of two parallel metal plates w/vacuum or air as dielectric

Small polythene spacer could be used to separate the plates

Capacitance

A = Area of the plate

d = Separation between the plates

Experimentally, C0  C, i.e. C0 = C + CS

CS = Stray capacitance

The connecting wires form extra capacitors

Each plate of the capacitor forms another cap. w/earth and other conductor

### Energy

A cap. w/capacitance C and charges Q, voltage across the cap.:

Work done to put extra charge Q onto the cap:

Energy stored in the capacitor w/charge Q, capacitance C is:

Total energy supplied by the battery = CV 2

Energy dissipated =

Independent of resistance of the circuit

Energy stored =

### Discharging through Resistor

VC = VR

Rate of discharge ( Charge remain in C

where: Initial charge in capacitor = Q0

By defining the Time Constant ,

Initial discharging rate:

Q in capacitor decreases exponentially

At half-life, charges in cap. =

Half life: t1/2 = RC ln 2

Voltage across C:

Discharging current:

V across the cap. and I of discharging also undergo exponential decay

### Charging through Resistor

VC + VR = V

where: Initial charge in capacitor = Q0

Initial discharging rate:

Half charged cap. :

Time to being half charged: t1/2 = RC ln 2

Voltage across C:

Voltage across R:

Current in circuit:

A capacitor can be charged up at a constant rate by using a rheostat to adjust the resistance during charging

### Capacitive network:

Connected in Parallel:

Caps in parallel = Caps w/conductors of larger area

Total capacitance = C

Charges in network = Q

All caps have the same voltage, but those with larger capacitance bear more charges

Plates joined together have the same polarity of charge

Connected in Series:

Caps in series = Caps sharing the charges = Caps sharing the voltage across

Overall voltage = V

Overall capacitance =

When caps connected in series, the charge Q in each capacitor / plate is the same

The charges stored in the series is equal to that stored in one cap

Plates joined together have equal but opposite charges

Larger cap have lower voltage

If two capacitors in series are connected to a battery:

Circuit:

Voltage are shared:

If two capacitors forms a loop:

Circuit:

Charges are shared: C ( Q

Before sharing: Total energy

After sharing:

Energy dissipated = E0 – E

## Magnetism

Magnetic field is a region of space in which a magnetic force exists

Field lines represent the strength & direction of a magnetic field

Field lines form loops, starting from N-pole and end at S-pole

Neutral point is a point where the resultant magnetic field = 0

### Magnetic flux

Force F on a conductor magnetic field ( Current I in it and length   to the field

F ( I 

B = Field strength

If the conductor // field, force = 0

Field strength = Magnetic induction

Unit: Tesla, T, NA–1m–1

Flux is the amount of field across an area perpendicular to B

 unit: Weber (Wb), NmA–1

Magnetic flux density is the force acting per unit length per unit current on a current-carrying conductor perpendicular to the field lines.  It indicates the strength of a effective magnetic field.

### Turning Effect:

When a coil in a B-field:

Force on PQ:

Force on SR:

Torque  = Fd = IabB = IAB
		where: A = ab = The area of the coil

If the coil’s normal makes an angle  with B-field,
		 = IAB sin

If the coil has N turns,  = BIAN sin

When : Plane // B-field,  attains maximum ( = BIAN)

When  = 0: Plane  B-field,  attains minimum ( = 0)

### Galvanometer:

A rectangular copper wire coil is wound on a soft iron core

The coil is in radial magnetic field

The B-field strength is constant when the coil turns

Deflection angle  ( Current I

The coil is restrained in its rotation by a hair spring

A restoring moment c is provided

At equilibrium,

Current sensitivity

If the galvanometer is used as a millivoltmeter, voltage sensitivity

R = Resistance of the coil

The sensitivity can be increased by:

Stronger magnet and narrower air gap (for a stronger B-field)

Use a coil with larger area (inc. A)

Use a coil of more turns (inc. N)

Weaker hair spring (dec. c)

### Charged particles:

A particle with charge q moving at velocity v in B-field

Force acting on it:

As F  V, no work is done

If V  B, F may act as a centripetal force

Period

If V makes an angle  with B, the path is helical

The superposition of circular motion and linear motion

Circular motion: Tangential velocity vc = v sin

Linear motion: Velocity v = v cos

### Comparison of Elect. F & Mag. F on charged particles:

| Elect. F on charged particle | Mag. F on charged particle |
| --- | --- |
| Force // Field | Force  Field |
| F is independent of v | F ( v |
| Work done ( 0 | Work done = 0 |

### Velocity Selector:

E field  B field

When a charged particle w/velocity v goes into velocity selector, B-force opposite to E-force

If , i.e. E-force = B-force, the route is undeflected

### Hall effect

A current passing thou’ a conductor in +y direction and a B-field in –x direction

A force occur in +z direction

The charge-carrier drift to the top surface due to the force whatever its +ve or –ve

The charge that the carrier bears accumulates on one edge and the opposite charge accumulate on the other edge

Potential difference set-up

Electric field set-up

Electric force by E-field is opposite to magnetic force by B-field

Before the equilibrium of E- and B-forces, the charges continue accumulating

The equilibrium reached, E-force = B-force

Current flows straightly w/o deflection to +y direction

At equilibrium,  qE = qvB

Hall voltage = Voltage btw the edges in equilibrium

qE = qvB  (  E = vB  (  VHall = Ed = Bvd

n = Number density of charge carrier
t = Thickness of conductor

For constant I,

 = Current density = 
d = Height of conductor

For constant , V ( d

Hall probe: A device used for measuring and comparing the direction and magnitude of a magnetic field

Consists of :	A slice of doped semi-conductor
 					A potentiometer to set zero for B-field = 0
 					Millivoltmeter to detect VHall

After calibration, B:V ratio is known

where B = B-field strength

The millivoltmeter should have very high resistance

The balancing potentiometer is used to make x, y in exactly opposite

### Search coil

A coil with N turns enclosing an area A

Measures the peak value of an alternating magnetic field

If the coil is in an alternating B-field, induced e.m.f. set-up

where V0 = Peak voltage;	 = Ang. freq. of alt. B-field

V0 = NAB0, B0 ( V0		where B0 = Peak B-field strength

B0 is read by connecting to a CRO

Sensitivity is increased in a high frequency

### Field strength

Long wire:

Flux lines from concentric circles

If the wire is infinitely long, B field strength at any point:

r = Distance from the wire;	0 = Permeability of free space

Solenoid:

If the solenoid consists of n turns, field inside the solenoid: B = 0nI

Circular coil:

Field at center of the coil:

Field in coil: Follows right hand grip rule

Field outside the coil: Opposite direction

## Electromagnetic induction

### Flux:

Flux of a coil of area A perpendicular to B field:   = BA

If the coil consists of N turns, flux linkage = N = NBA

### Faraday’s Law:

When a conductor is under a B-field and its flux linkage is changing, a EMF is induced in it

Faraday’s law:

Lenz’s law: An induced current flows in such a direction as to opposite the change of flux which causes the current to flow in the first place.

### Induced EMF:

Straight conductor:

Conductor with length , moving at velocity v perpendicular to B

Spinning disc:

A circular disc of radius r, rotating at angular frequency 2f perpendicular to B-field

 = r2fB

Flow of current: Center (Neg. pole)  Rim (Pos. pole) External circuit  Center

Rotating coil

A coil of area A with N turns under B field

Rotating with angular frequency  about an axis  to B-field

 = BANsin t

 =  0sin t		where 	 0 = BAN

### AC generator:

A rectangular coil with area A of N turns rotating at angular velocity  in B-field

 = BA cos

 = t

 =  0sint 	where   0 = BAN

When  = 0,	 = 0

When ,	 =  0 (Maximum)

DC generator produces fluctuating DC

Spinning disc can give a steady DC

### Back EMF

A current applied to a motor, coil turns

Coil turns in B-field, back EMF  set-up

 against V

Power input:	Pin = VI			Power output:	Pout = I

Power loss:	Ploss = I 2R

Energy dissipated in coil resistance

V =  + IR

Torque in coil:

Pout =  = NBAI

 = NBA

Maximum power output:

Max. power output attains when

### Eddy current:

If magnetic flux thou’ a conductor / a part of conductor changes, current may circulating throughout any loop of the conductor

Eddy current

Eddy current is in the direction follows the Lenz’s law

I may be very large as R is very small

Eddy current causes heating effect on material

A sample can be heated by rapidly changing B-field

The changing B-field can be produced by a high frequency AC

Applied for cases that is impossible to make thermal contact (e.g. in vacuum)

Example of application: Induction heater

### Transformer

Using 1° and 2° coils wound on a laminated soft iron core

AC in 1° coil  Changing flux EMF in 2° coil

Mutual induction

Ideal transformer:

1° coil: Supplied voltage = VP;  No. of turn = NP
2° coil: Output voltage = VS;  No. of turn = NS

Back EMF:

 is identical on both coils

EMF in 2° coil:

Output voltage = S = VS



Voltage ratio = Turns ratio

2° current is small

Flux leakage = 0

1° resistance and current are small

Practically, resistance rP & rS exists in 1° & 2° coils

VP = P + IP rP		VS = S + IS rS

### Inductor

Current changing in inductor

Back EMF

Self-inductance:

L always positive

Unit: Henry (H), VA–1s, WbA–1

A measure of opposition to a changing current

A solenoid of air core with length , turns per unit length, cross-sectional area A

L = 0n2A

L depends on:	(	Dimension of coil

Number of turns

Permeability of core material

### L-R circuit:

Battery EMF + Back EMF = Voltage across R

t = 0,  I = 0,

as	 t  0;

After switching on the circuit,

Time constant

After switching off the circuit,

Energy is stored in the B-field thou’ the coil

,  Electrical energy applied E = I dt = LI dt

Energy stored in L = Electrical energy supplied =

### Comparison of Inductor & Capacitor:

| Inductor | Capacitor |
| --- | --- |
| Stores energy in B-field | Stores energy in E-field |
| Energy: | Energy: |
| Time constant: | Time constant:  = CR |

## Alternating Current

### Alternating current:

Current: I = I0sin t		where I0 = Peak current;  = Angular frequency

Root-mean-square value: ;

Mean power consumption: ‹P› = Vrms Irms cos		where  = Phase difference btw V & I

If V & I are completely out of phase, no power is consumed

The power below 0 is returned to the power supply

Freq. of power variation = 2 Freq. of current variation

For any phase difference, ‹P›

### Single component circuit:

R circuit (Resistive circuit)

Power: ‹P›

Phasor diagram:

V, I in phase

C circuit (Capacitive circuit)

Power consumption = 0

Reactance:

Unit: Ohm ()

Phasor diagram:

I leads V by 90°

L circuit (Inductive circuit)

Power consumption = 0

Reactance:

Phasor diagram:

V leads I by 90°

CIVIL – C: I leads V; L: V leads I

In capacitive circuit, I ( ;	in inductive circuit,

In capacitive circuit, ;	in inductive circuit,

### Two component circuit:

RC circuit

V0 =	Peak voltage supplied by the AC source
VR0 =	Peak voltage across the resistor
VC0 =	Peak voltage across the capacitor

I leads V by ,		where

Impedance:

V0 = I0 Z

Power consumption: ‹P›

The value, cos , is called the Power factor

Phasor diagram:

LR circuit

V leads I by ,		where

Impedance:

Power consumption: ‹P›

Phasor diagram:

LC circuit (LC oscillator)

Charged cap Current thou’ L

Back EMF by L  Charging C

Oscillation on the flow of current

Charge on C:	Q = Q0 cos(t + )
Current on circuit:	I = Q0 sin(t + )

Frequency of oscillation:

Energy in C: 
Energy in L:

Total energy in the circuit:

Phasor diagram:

### Filter:

Used in AC circuits to modify the characteristics of time-varying signals

In a RC circuit:

For low freq., most applied voltage appears across the cap
For high freq., most applied voltage appears across the resistor.

Connecting output across R gets a high-pass filter;
Connecting output across C gets a low-pass filter

In a LR circuit:

VL0 = IXL = IL,

For low frequencies, most applied voltage appears across the resistor
For high freq., most applied voltage appears across the inductor

Connecting output across L gets a high-pass filter;
Connecting output across R gets a low-pass filter

In a LC circuit

For low freq., most applied voltage appears across the capacitor;
For high freq., most applied voltage appears across the inductor

Connecting output across L gets a high-pass filter;
Connecting output across C gets a low-pass filter

In loudspeaker, woofer is connected to the low-pass filter;
and the tweeter is connected to the high-pass filter

### RLC circuit:

Impedance

V0 = I0Z; 	V02 = VR2 + (VL – VC)2

Average power: ‹P›

;	;

If XC = XL, then VC = VL

V0 by AC source is in phase with I0

Z = R = minimum

maximum

Electrical resonance attains when XC = XL,

Phasor diagram:

Phase difference  satisfies

 approaches toward  as the frequency increases to infinity

### Rectification:

Diode: Conducts current only in forward bias

Half-wave rectification:

Circuit:

RMS output voltage:

Waveform:

Full-wave rectification:

Circuits:

Bridge full-wave rectifier:

Center-tap full-wave rectifier:

RMS output voltage:

Waveform:

Peak voltage of rectified DC < Peak voltage of rectified AC

Smoothing circuits

Smoothing circuit:

Current inc.	  C charged up

Current dec.	  C discharged

Smoothed the decrease of I in output

The capacitor is called the “reservoir capacitor” or “storage capacitor”

Waveform of the smoothed DC:

The smoothed current are with ripples

The ripples can be regarded as the superposition of a DC and an AC

DC can be regarded as an AC with  ( 0

For AC, XL = L is larger

Filter across L = AC component of the smoothed DC

For DC, XC is larger

Filter across C = DC component of the smoothed DC

The capacitor is called the “filter capacitor”

Filtering circuit:

## Electronics

### Semiconductors:

Semiconductors has a resistivity btw a conductor and insulator

Conducts current a little bit

Silicon has a giant covalent structure

If a certain amt of energy is supplied to the covalent bond, it breaks

The sharing electrons is then detached and able to move about

In higher temperature, more bonds breaks due to thermal motion

Resistivity dec. as temperature inc.

Very pure semiconductors: Intrinsic semiconductors

If some Gp.V element like phosphorus is added to semiconductor as impurity,

Fifth outer e– of the impurity is quite free to move about

The free negative e– can be a charge carrier for conducting

n-type semiconductors

If some Gp.III element like boron is added to semiconductor as impurity,

The lack of the fourth outer e– makes a mobile ‘hole’ in the bonding

The hole is the lack of a negatively charged electron, it may be regarded as a positive hole

p-type semiconductors

When a n-type and a p-type semiconductors are connected, a p-n junction is formed

If p-type is at higher potential than n-type

The positive holes will move across the p-n junction to the n-type region

The negative electrons will move across the p-n junction to p-type region

The junction conducts, i.e. in forward bias

If n-type is at higher potential than p-type

The positive holes will move away from the p-n junction and crowded at the p-type region

The negative e– will move away from the p-n junction and crowded at the n-type region

Nothing moves across the junction

The junction does not conducts, i.e. in reversed bias

Since current flows only in one direction, it forms a semiconductor diode

### Diode:

Ideal diode:

In forward bias, current thou’ it can be arbitrarily large and p.d. across is negligibly small

P.d. across diode in forward bias Vf , is called forward voltage

In reversed bias, current I = 0 for any negative p.d. across diode

Practically,

No current flows across the diode if p.d. across  0.6V

When p.d. is 0.6V – 0.8V, the current thou’ increases rapidly

Max. p.d. across the diode = 0.8V, even for a large current

If the diode is in reversed bias, there is a small leakage current of 10–8A

In extreme negative p.d., the diode will conduct

That p.d. is called breakdown voltage

When breakdown, power consumption in diode is very large and it will burn up

### Transistor (n-p-n):

Consists of Base, Collector and Emitter

Collector, emitter: N-type semiconductor

Base: P-type semiconductor

If VBE  0.5V, the transistor conducts no I

If VBE  0.5V, the transistor is conducting

IB increases rapidly from 0.5V onwards

VBE stays constant at 0.7V even IB has further increase

Resistance across BE is of the order of k

If VCE is fixed, IB ( IC

IC = IB

Current amplification factor:

 is constant for a particular transistor

IB & IC are in proportion only if IB is not too large

IE = IC + IB ( IC	(as IB  IC)

In practice, a resistor RB is connected to the base

Limits the base current IB and prevent damage to the transistor

Enlarge the adjustment for a current change in potentiometer

Keeps the collector current IC below its maximum allowed current

### Saturation

If a load resistor RL is connected in series with collector,

For small IB, IC = IB

When IB exceed a limit, IC saturates and no longer increases

When saturation occurs, VCE ( 0

IC ( Max. IC =

IB when saturation starts =

### Input-Output Voltage Characteristic

Input voltage: Vin = IBRB + VBE

Output voltage: Vout = VCE = Supplied V – ICRL

Cut-off state:

When VBE  0.5V,  IB = 0 and IC = 0

(Vin  0.5V,	IC = 0,	Vout = Supplied voltage

Saturation:

When Vin exceed a certain value, IB is large enough to make the collector saturates

During saturation, Vout ( 0

Linear region:

Before saturation and above 0.7V, IC = IB

Vin varies linearly with Vout

Voltage gain:

Application:

Linear region: Linear voltage amplifier

Cut-off & Saturation: Digital circuit / Logic gates

### Operational Amplifier:

An analog IC w/8 pins, only five are often used

A power source is required:

Applied positive voltage:	+VS = +15V

Applied negative voltage:	–VS = –15V

Possess two input (V+, V–) and one output (Vout)

It has a high input impedance of about 2 M

draws only a very small current from the input

It has a low output impedance of about 70-100 

large output power can be obtained

It has a high slew rate of 106 - 107 Vs–1

responds quickly to a.c. inputs up to several MHz

It has a large voltage gain

inputs can be greatly amplified

Output voltage depends on the difference of input voltages

Vout ( (V+ – V–)

Vout = Ao(V+ – V–)

Ao = Open-loop voltage gain of the op amp, of the order 105

Linear relationship holds until it saturates when Vout ( VS

Actually, op amp saturates at Vout ( (13V  &  V+ – V– = (65V

V– is called the inverting input as Vout = Ao(–V–)	when  V+ = 0

V+ is called non-inverting input as Vout = Ao(V+)	when  V– = 0

In open-loop, the use of op amp is limited since the voltage gain:

Too high s.t. it becomes saturated easily

Sensitive to temperature changes

Decreases greatly with input frequency

Varies a lot for the same code of op amp

### Negative feedback:

Output Vout is fed back to the inverting input V– via a feedback resistor Rf

Closed-loop mode

When V+ is earthed, input current Iin = Feedback current If

Virtually, Iin = If

Current flowing into the op amp is negligibly small

Current across (  ( 3(10–11A

The closed-loop set up forms a feedback amplifier

The input voltage Vin and output voltage Vout forms a Z-shaped curve

Vout is in antiphase with Vin

P.d. across Rin = IinRin = Vin – V– ( Vin		as V– ( 0 before op amp saturates

P.d. across Rf = IfRf = V– – Vout ( –Vout

Since Iin ( If as op amp draws negligible current,
		Slope of linear region  A 

A is called the closed-loop voltage gain

Rf = Rin, the circuit is an inverter s.t. Vout = –Vin

Advantages of feedback over open-loop:

Voltage gain is independent of intrinsic properties of op amp

Voltage gain is predictable and can be controlled by Rf & Rin

Voltage gain is more stable to temperature and frequency fluctuations

A is constant from 0 to 10kHz but Ao will decrease by the factor 10–2

Linear region is much wider than open-loop circuit

Several V for feedback whereas 65V for open-loop

### Non-inverting input:

Input voltage connects to the non-inverting input instead of the inverting input

Vin = V+

R & Rf act as a potential divider:

Since Vin = V+ ( V– ,

Multiply the input by a constant factor

Multiplier circuit

### Application of Op Amp:

Summing amplifier

Input current: Iin = IA + IB =

Feedback current: If =

( impedance of op amp is high, Iin = If

The circuit multiplies the input voltages by different factors and then adds them

Summing amplifier

Connecting the summing amplifier and inverter circuit, a subtractor forms

Voltage follower

In the multiplier circuit, if Rf = 0 or R ( (, Vout = Vin

Voltage follower circuit

The input impedance of the op amp is high

The circuit can be used as a high resistance voltmeter

Reproduce the input voltage accurately

Can measure the p.d. across a capacitor w/o let it discharge

If a load rheostat RL is connected to the output, and the op amp is of input impedance r,

(V+ – V–) = Iinr

Vout = Ao(V+ – V–) = AoIinr

Vout = IoutRL = AoIinr

D.C. amplifier

If RL is too small, Vout will drop significantly

Comparator

In open loop configuration, Vout saturates if difference in input voltage  65V

If V+ and V– is connected to different potential, it will give a saturated output easily

If V+  V–: Vout is positive

If V–  V+: Vout is negative

A digital device that compares the inputs

# Footnotes

Electric field intensity = Electricity field strength

Permittivity of free space = Permittivity constant

Current density = Current per unit cross-sectional area

Jockey = A sliding contact

Power loss = Ohmic loss

High-pass filter: Passes voltage (signals) of higher frequency while low frequencies are filtered (attenuated)

Example of semiconductor: Silicon, Germanium

Current amplification factor = Current gain

Linear region = Amplification range

Slew rate = The rate at which the output voltage can changed when the input voltages are changed